## Slide 1: High Resolution Turbine-Specific Matrix
Practical Requirements and Examples

## Slide 2: Current DNV GL treatment of turbine performance
Use global TI vs WS matrix to capture “outer” effects
Use global PPT results to capture “inner” effects

## Slide 3: 80%* of people think their turbines are better than average, how can we give credit to this?
We need representative data to demonstrate turbine performance over a range of conditions.
Ideally, the direct relationship between turbine performance and the warranted/sales power curve is able to be understood (rather than needing a two step process)
*statistic fictionalized for effect
Not all turbines are better than average!
Notes: 5 or more turbines so the combined error is close to, or lower, than our standard assumptions of 2%-2.5%

## Slide 4: Required: Individual Turbine Performance Matrixes based on the raw data collected during multiple power performance tests
Minimum number of tests required for building a representative matrix?
Combined results must be demonstrated to be stable
  “Round Robin” tests with provided data should show consistent results.
  Relatively low scatter within matrix bins and between tests
  Substantial deviations will need explanation
Representative of target site conditions
  The majority of relevant WS-TI cells should be calculated using data rather than modelled or fitted data.

## Slide 5: Additional considerations when comparing directly to warranted/sales PC (largely addressing “inner range” differences)
Seasonally representative
  We need representative data from all seasons to capture known varibility of “inner range” performance
Geographically diverse
  For broad application, need to demonstrate that matrixes produced in different regions, or conditions (offshore, forestry, etc.) show consistent results.

## Slide 6: Example case 1
Rotor size | Power Curve Revision |  | 
 | A | B | C
Smallest | 1 |  | 
Medium | 2 |  | 
Large | 2 | 1 | 1
Extra large | 1 |  | 
Data:
  8 PPT tests on the same platform, but few tests on the same configuration
  Limited seasonal coverage, reasonable geographic coverage
Aim:
  Derive platform-specific matrix for use on all projects

## Slide 7: Example case 1
Q1: Can we combine tests with different rotor diameter and control strategies to understand the performance of the platform?
  Limited data, but good indications when comparing to normalized PC
Q2: Do the tests behave like our larger data set?
  Yes, when compared to normalized PC
Q3: Do the tests imply that we should be treating the platform differently than other turbines?
  Possibly. Data gives higher confidence that we are predicting relative turbine performance accurately, but lack of seasonal data means we can’t directly opine on gross performance.
Combined results must be demonstrated to be stable
Representative of target site conditions
Seasonally representative
Geographically diverse

## Slide 8: Example case 2
Q1: Do the tests behave like our larger data set?
  Yes, when compared to normalized PC
Q2: Do the tests imply that we should be treating the platform differently than other turbines?
  Almost. There is enough information to develop a performance matrix which directly references the warranted/sales power curve, however the lack of seasonal representative data means we can’t use results quantitatively.
  While the data is not geographically diverse, this isn’t an issue because the intent is to apply it to a nearby project.
Combined results must be demonstrated to be stable
Representative of target site conditions
Seasonally representative
Geographically diverse
Data: 9 PPT nearby (<150 km) of a new project, same turbine type
Aim: Derive platform- and region-specific WS-TI matrix for nearby projects

## Slide 9: Can individual manufacturers differentiate themselves with turbine specific data? - Practical Considerations
Where should the thresholds be set to balance data availability and robust analysis?
    Minimum data requirements for IEC tests are not sufficient for developing a matrix.
Turbine models are evolving more quickly than we can test them.
  Can we use previous generations to inform current generations?
  Normalize to Zero TI PC?
Seasonality of test results
  Why do ‘inner range’ test results vary by season?
  Are year-long data sets practical?

## Slide 10: Thoughts? Comments?
Taylor Geer, Carl Ostridge, Josiah Mault
taylor.geer@dnvgl.com, carl.ostridge@dnvgl.com, Josiah.Mault@dnvgl.com