## Slide 1
PCWG Intelligence Sharing Initiative Update
29 September 2016
Minneapolis, US
Andy Clifton (NREL)

## Slide 2
Motivation:
PCWG-Share-X: What are we Trying to Achieve?
There are currently many candidate methods for predicting turbine performance in outer range conditions, but no consensus about which method works best.
The industry has a wealth of historic power performance data whose full potential is yet to be realised.
Solution:
The Power Curve Working Group Intelligence Sharing Initiative (PCWG-Share-X) aims to objectively test many methods for predicting outer range turbine performance in order to determine which works best.
The Power Curve Working Group Intelligence Sharing Initiative (PCWG-Share-X) aims to unlock the full value of our industry’s data.
The PCWG Intelligence Sharing Initiative enables the industry to pool the value of many datasets without actually sharing any commercially sensitive data.

## Slide 3
PCWG-Share-X Definition Document
Download PCWG-Share-01 Definition Doc from www.pcwg.prg
Everything you need to know about PCWG-Share-X

## Slide 4
Inner Range Power Curves Extracted from the Dataset Itself: the data analysis process has been designed such that the warranted power curve is never considered. Instead a power curve is extracted from a subset of the data (Inner-Range) which is then used to model the power output in the outer-range.
Intelligence Sharing, not Data Sharing: the data analysis process has been designed such that the datasets do not need to be shared outside of the participant organisations. Instead of sharing the actual data, participants will share performance metrics which describe the accuracy of the trial methodologies.
PCWG-Share-X: Neutralising Commercial Sensitivities

## Slide 5
Proprietary Dataset D
Analysis Definition Y
Organization D
Proprietary Dataset A
Organization A
Proprietary Dataset B
Organization B
Proprietary Dataset C
Organization C
Aggregator
(NREL)
Combination Analysis
Aggregated Hypothesis Performance Metrics
Hypothesis Performance Metrics
Analysis Definition Y
Analysis Definition Y
Analysis Definition Y
Hypothesis/Trial Methodology
How well did the trial method perform?
PCWG-Share-X: Data Flow

## Slide 6
PCWG-Share-X: Error Metric Definitions
See PCWG-Share-01 Definition Document for Further Details
For NME to be zero a method must be right on average
For NMAE to be zero a method must be right all the time

## Slide 7
PCWG-Share-1
≈50 participant datasets (4 remote sensing datasets)
3 method tested (REWS, IEC Turbulence Correction & Power Deviation Matrix)
Calculation Issues: Interpolation Errors and Erroneous Outliers
PCWG-Share-X Timeline
Dec 2015
Sept2016
Oct to
Dec
2016
PCWG-Share-1.1
Objective: to iron out the issues experienced during PCWG-Share-1
Two week turn-around
≈44 participant datasets (11 remote sensing datasets)
Same 3 method tested (REWS, IEC Turbulence Correction & Power Deviation Matrix)
Streamlined participation process
PCWG-Share-1 Calculation Issues Resolved
PCWG-Share-2
Objective: to test more methods and expand to more datasets
Target: 100 participant datasets (25 remote sensing datasets)
Additional methods to be tested e.g. 3D Power Deviation Matrix & REWS with Upflow
Refined results analysis

## Slide 8
PCWG-Share-1 vs PCWG-Share-1.
Erroneous Outliers: unexpectedly large errors for baseline inner range
Interpolation Issue: Smaller inner baseline errors still undesirable
PCWG-Share-1
Baseline Issues Resolved
PCWG-Share-1.1
Baseline normalised error i.e. before any correction
Spread of Baseline Outer Range Results, indicates why Outer Range Corrections are required

## Slide 9
PCWG-Share-1.1 Comparison of Methods (‘Four Cell’ Matrix)
Low Turbulence
High Turbulence
High Wind Speed
Low Wind Speed
Baseline
REWS
Turb Corr
REWS & Turb Corr
Power Dev Matrix
Baseline
REWS
Turb Corr
REWS & Turb Corr
Power Dev Matrix
Better
Better
Worse
Seek to determine which methods work well when.
PCWG-Share-2 to expand upon these results.
Worse
Percentage Reduction in Error

## Slide 10
PCWG-Share-1.1 Power IEC Turbulence Correction
(errors by wind speed)

## Slide 11
PCWG-Share-2 Proposed Plan
Proposed PCWG-Share-2 Methods:
REWS with Upflow (see August Pamplona proceedings for details).
3D power deviation matrix
All previous methods (REWS, Turbulence, 2D Power Deviation Matrix)
Proposed PCWG-Share-2 Timeline:
Mid-Oct: Release of Software with new methods implemented
Mid-Nov: Submission deadline
Mid-Dec: Presentation of results at December PCWG Meeting in Glasgow
Dataset Target:
100 participant datasets (25 remote sensing datasets)
Possible PCWG-Share-3 Methods
BEM based model: simple model or full aero-elastic (e.g. FAST)
Modified Turbulence Correction (see August Pamplona proceedings for details)
Machine Learning (black box approach?)
Production by Height?

## Slide 12
For Discussion
Making the Process Easier
What improvements could be made to make participation faster and easier?
Improvements to Error Metrics & Visualisations
What improvements could be made to how method errors are reported/visualised e.g. expressing by wind speed errors as fraction of total energy instead of bin energy
PCWG-Share-2 Methods
Have the right methods been proposed for PCWG-Share-2?

## Slide 13
Many thanks to all PCWG-Share-1.1 Participants
Join the Power Curve Working Group at: www.pcwg.org