## Slide 1
IEC 61400-12-1 FDIS 2016 Worked Examples
29th September 2016
Minneapolis, US
Ellie Weyer, AWS True Power

## Slide 2
PCWG Industrial Placement
The first PCWG Industrial Placement was completed by Andrew Lawrence of Cambridge University during July and August 2016.
The placement was sponsored by SSE, RES & Senvion.
The placement was hosted at RES’s office Kings Langley and managed by Lee Cameron (RES).
Andrew was tasked with completing a set of work examples of the uncertainty methodology of the new IEC 61400-12-1 standard.
This project is intended to be complimentary to the IEA Task 32 Uncertainty Round Robin
Many thanks to our supporting members who made this industrial placement possible

## Slide 3
IEC 61400-12-1 Edition 2 Status
The PCWG in collaboration with IEA Task 32 are seeking to build industry understanding of the new Power Performance Standard. www.pcwg.org.
Document Stage | Document Stage Description | Status
CDV Committee Draft for Voting | Feedback Stage: Document is sent to the various National Committees for comment. Once the feedback is received the TC (Technical Committee) integrated the feedback and prepares the FDIS. | Completed
FDIS Final Draft International Standard | Approval Stage: Document is sent to the National Committees for voting. At this stage no comments or requests for change are accepted although typographical errors can be pointed out for correction by IEC prior to publication. | Translation of FDIS to French followed by issue of English/French FDIS to national committees for voting in October.
Publication of IS (International Standard) | Final Stage: The IEC generates the cover pages and prepares the document for publication. The document is published and put on sale in the IEC Web Store. Note that editorial errors not captured prior to publication can still be issued as corrigendum by IEC throughout the life of a specific publication. | Expected Late 2016/Early 2017
Current Status

## Slide 4
IEC Task 32 & PCWG Collaboration Overview
The PCWG & IEA Task 32 are collaborating on a round robin exercise and associated set of spreadsheet worked examples:
IEC Task 32 is running a round robin on the application of IEC61400-12-1 Ed 2 using LiDAR data. The round robin will have particular focus on the uncertainty methodology of the new standard.
The PCWG is seeking to develop a set of worked examples showing how to apply the uncertainty method defined in the new standard. Once complete these worked examples will serve as both an educational tool and as a benchmark for the PCWG analysis tool.
Expected Outcome: The combination of the round robin and supporting work examples are intended to build industry understanding and consensus of the new edition of IEC 61400-12-1.

## Slide 5
IEA Task32 & PCWG Activities Timeline (2016)
Distribution of round robin dataset and instructions to participants.
Initial round robin results presented at Pamplona and Minneapolis PCWG meetings.
Second round robin initiated, results due by end of October.
Collation of final results
Presentation of final results at PCWG meeting in Glasgow.
Round Robin
Worked Examples
Preparation of work examples.
Presentation of full suite of worked examples at September PCWG Meetings. Release of worked examples on PCWG DropBox.
IEA32 & PCWG members to review worked examples and provide feedback.
Public publication of work examples after Dec PCWG meeting (www.pcwg.org)
Jul & Aug
Sept
Oct
Nov
Dec

## Slide 6
IEC 61400-12-1 FDIS 2016 Worked Examples

## Slide 7: Worked Examples Objective
We aim to demonstrate the proper implementation of the new IEC power performance testing standard, with focus on the uncertainty calculation.
We aim to do this by creating a collection of Excel spreadsheet calculations for key sections.
The calculations will be modular in structure, each showing the method for a small section.

## Slide 8: Worked Examples Objective
We aim to demonstrate the proper implementation of the new IEC power performance testing standard, with focus on the uncertainty calculation.
We aim to do this by creating a collection of Excel spreadsheet calculations for key sections.
The calculations will be modular in structure, each showing the method for a small section.

## Slide 9: Power Curve Uncertainty Calculations
Uncertainty combination
Equation E.8 in the standard gives the method for combining separate uncertainty contributions to give overall uncertainty
This is the AEP uncertainty. It is what we need to calculate!

## Slide 10
Uncertainty combination
Equation E.8 in the standard gives the method for combining separate uncertainty contributions to give overall uncertainty
Hours in a year. This turns our uncertainty in power into and uncertainty in energy
Power Curve Uncertainty Calculations

## Slide 11: Power Curve Uncertainty Calculations
Uncertainty combination
Equation E.8 in the standard gives the method for combining separate uncertainty contributions to give overall uncertainty
Many components vary with wind speed so the combination is performed across all bins of the power curve

## Slide 12: Power Curve Uncertainty Calculations
Uncertainty combination
Equation E.8 in the standard gives the method for combining separate uncertainty contributions to give overall uncertainty
Relative occurrence of each wind speed bin (to account for long term wind speed distribution)

## Slide 13: Power Curve Uncertainty Calculations
Uncertainty combination
Equation E.8 in the standard gives the method for combining separate uncertainty contributions to give overall uncertainty
Category A uncertainties
Statistical uncertainties, based on the data. Due to statistical scatter, do not account for potential bias.
Category B uncertainties
To reflect potential bias in instrumentation and due to methodology.

## Slide 14: Power Curve Uncertainty Calculations
Uncertainty combination
Equation E.8 in the standard gives the method for combining separate uncertainty contributions to give overall uncertainty
Category A uncertainties
Statistical uncertainties, based on the data. Due to statistical scatter, do not account for potential bias.
Category B uncertainties
To reflect potential bias in instrumentation and due to methodology.
We have a made spreadsheet demonstrating the calculation of each category A and B uncertainty component

## Slide 15: Power Curve Uncertainty Calculations
Category A - Power
“Power Curve Measurement Using The Method of Bins.xlsx”
Simple and well understood
  Related to the standard deviation in each power curve bin

## Slide 16: Power Curve Uncertainty Calculations
Category A - Site Calibration
“Site Calibration Using Linear Regression.xlsx”
New in this issue of the standard
Based on “K-Fold Analysis”:
  Break the site calibration filtered dataset into 10 subsets (“folds”)
  Predict turbine mast wind speed for each subset using the calibration data from the other 9 folds
  Uncertainty is based on the standard deviation of prediction error in each fold

## Slide 17
Category B - Power
“E.5 Category B Uncertainty in Electric Power.xlsx”
Uncertainties due to:
  Current and voltage transformers
  Power transducer
  Data acquisition
Depends on the classification of voltage and current transformers
  IEC 60044-1 gives uncertainties for different class of current transformers
  IEC 60688-1 gives uncertainties for different class power transducers
Power Curve Uncertainty Calculations

## Slide 18
Category B – Wind Speed
“due to hardware used”, i.e. WS measurement instrumentation
For cup or sonic anemometer:
Components due to:
Pre-test calibration,
post-test calibration
Classification
Mounting
Lightning Finial
Data acquisition system
Power Curve Uncertainty Calculations
Notes: REWS is not a piece of hardware, rather it is a definition of wind speed measurement. You can measure this using either mast or RSD in theory, although only RSD is practical.

## Slide 19
Category B – Wind Speed
“due to hardware used”, i.e. WS measurement instrumentation
For RSD:
Components due to:
Verification test vs mast
In-situ comparison to mast
RSD classification
Mounting
Flow variation in the measurement volume
Monitoring of the RSD
Power Curve Uncertainty Calculations
Notes: REWS is not a piece of hardware, rather it is a definition of wind speed measurement. You can measure this using either mast or RSD in theory, although only RSD is practical.

## Slide 20: Power Curve Uncertainty Calculations
`
Category B – Wind Speed
Uncertainties due to:
  Hardware used
    "E.13.4 Category B uncertainty in wind speed from cup or sonic.xlsx"
    "E.13.5 Category B uncertainty in wind speed from RSD.xlsx"
    "E.13.6 Category B uncertainty in wind speed from REWS.xlsx"
      Note that REWS can in theory be measured with mast or RSD, in reality only RSD is practical
  Terrain
    "E.13.11 Category B uncertainty in wind speed from flow distortion due to terrain.xlsx“
    Related to the site calibration (or lack thereof)
  Air Density Correction
    "E.10 Category B uncertainty in Air Density.xlsx"
    Related to air density correction
"E.13.3 Category B Uncertainty in the Wind Speed Measurement.xlsx"
Notes: REWS is not a piece of hardware, rather it is a definition of wind speed measurement. You can measure this using either mast or RSD in theory, although only RSD is practical.

## Slide 21
Category B – Temperature, Pressure and Relative Humidity
    "E.10 Category B uncertainty in Air Density.xlsx"
Relative humidity was not included in the previous standard
Same components, but sensitivity factor has changed in this issue of the standard
All informed by manufacturer specs with extra penalties if measurement is far from hub height
Temperature:
Calibration
Shielding
Mounting
Data acquisition
Relative Humidity:
Calibration
Mounting
Data acquisition
Pressure:
Calibration
Mounting
Data acquisition
Power Curve Uncertainty Calculations

## Slide 22
Category B – Method related components
    "E.13.15 Category B Uncertainty Calculation for Method related components.xlsx"
Many new sub-components in this issue of the standard
Uncertainties due to:
  Uncertainty in calculation of wind shear & veer
  Uncertainty due to lack of knowledge of upflow angle & turbulence
  Uncertainty due to unquantifiable seasonal effects
  Uncertainty due to cold climate
  Uncertainty due to turbulence normalisation
Power Curve Uncertainty Calculations

## Slide 23
  REFERENCES
  [1] Lawrence, A., (2016), Power Curve Measurement Using Method of Bins, RES CALCULATION, TC01-037758, Issue 01
  [2] Lawrence, A., (2016), Site Calibration Using Linear Regression
  [3] Lawrence, A., (2016), E.5 Category B Uncertainty in Electric Power
  [4] Lawrence, A., (2016), E.13.3 Category B Uncertainty in the wind speed measurement
  [5] Lawrence, A., (2016), E.10 Category B Uncertainty in Air Density
  [6] Lawrence, A., (2016), E.13.15 Category B Uncertainty for Method related components
PCWG Drop Box Folder
Email PCWG@res-ltd.com for access.
Email Feedback to PCWG@res-ltd.com.

## Slide 24
Email Your Feedback to PCWG@res-ltd.com.
Worked Example Feedback Tracker
Feedback Tracker Spreadsheet can be found in DropBox next to the worked example spreadsheets.

## Slide 25
Join the Power Curve Working Group at: www.pcwg.org