## Slide 1
PCWG 2016 Update
Wednesday, 13 December 2016
Glasgow, Scotland
Peter Stuart

## Slide 2
We’ve Always Known that Real World Wind Turbine Performance is NOT as Simple as Power=P(v, ρ)!
Extract from C.J. Christensen et al: ”Accuracy of power curve measurements”, Risø-M-2632, 1986...
”… The power curve is then seen as the relation between the power P(v) produced by this undisturbed wind v.
This definition is, however, of very doubtful value for a windmill in the natural wind. The main difficulty is that it assumes a smooth laminar flow of high degree of homogeneity and symmetry”
Power (P)
Wind Speed (v)
P=P(v, ρ)
ρ = Air Density
The PCWG aims to build industry consensus on how best to predict real world turbine performance and look beyond P=P(v, ρ). www.pcwg.org.

## Slide 3
Categories of Turbine Performance Corrections
Inner Range Performance
Adjustments to reflect the fact that even under warranted/ideal conditions performance may not be 100%
Outer Range Performance
Adjustments to reflect the fact that turbine performance may deviate from Inner Range behaviour in Outer Range Conditions
e.g. Low/High TI, Low/High Shear etc.
Note: The PCWG Inner-Outer Range Proposal is Conceptual Decomposition, and does infer specific parameter ranges.
Reflecting the Real World…
+ Other Performance Corrections
Icing, Blade Degradation, Sub-optimal performance etc.
Inner Range
Outer Range

## Slide 4
Reflecting the Real World: Inner Range Performance
Extract from ‘High Resolution Turbine-Specific Matrix’, Carl Ostridge DNV GL,
Colorado PCWG Meeting, 10 August 2016, download from www.pcwg.org.
Historic Performance Under Inner Range Conditions
The PCWG is seeking to design an adjustment framework to define how to make best use of historic power performance tests when predicting future turbine performance.

## Slide 5
Turbulence Intensity [%]
Wind Speed [m/s]
Colour = % Observed Power Deviation
(Observed - Base)
Power (P)
Wind Speed (v)
P=P(v, ρ)
Inner Range Performance
Outer Range Deviations (Observed – Base)
High TI & High V
Negative Deviation
Low TI & Low V
Negative Deviation
High TI & Low V
Positive Deviation
Reflecting the Real World: Outer Range Performance
The PCWG is attempting to evaluate methods for predicting Outer Range performance via the PCWG Intelligence Sharing Initiative (PCWG-Share-X)

## Slide 6
21 PCWG Meetings Later…
The PCWG has been meeting since December 2012 and has held a total of 21 meetings in Europe and the US. It currently has a membership of over 300 people.
http://www.pcwg.org/proceedings/2012-12-04/WTWG-04Dec2012-01-MA-RES-Power-Curve-Workshop-Introduction.pdf
At the first presentation at the first meeting it was noted how the ‘building blocks’ for solving the issues at hand already existed.
Today, this ‘building blocks’ statement is truer than ever!

## Slide 7
Far from Consensus
Where is the PCWG on the issue of turbine performance in outer range conditions?
Technical Dimension
Political Dimension
Far From Certainty
Close to Certainty
Close to Consensus
2014 Results

## Slide 8
Technical Dimension
Political Dimension
Far From Certainty
Close to Certainty
Close to Consensus
Far from Consensus
Where is the PCWG on the issue of turbine performance in outer range conditions?
2015 Results

## Slide 9
PCWG Intelligence Sharing Initiative Update
PCWG-Share-1.1

## Slide 10
Motivation:
PCWG-Share-X: What are we Trying to Achieve?
There are currently many candidate methods for predicting turbine performance in outer range conditions, but no consensus about which method works best.
The industry has a wealth of historic power performance data whose full potential is yet to be realised.
Solution:
The Power Curve Working Group Intelligence Sharing Initiative (PCWG-Share-X) aims to objectively test many methods for predicting outer range turbine performance in order to determine which works best.
The Power Curve Working Group Intelligence Sharing Initiative (PCWG-Share-X) aims to unlock the full value of our industry’s data.
The PCWG Intelligence Sharing Initiative enables the industry to pool the value of many datasets without actually sharing any commercially sensitive data.

## Slide 11
PCWG-Share-1.1 Comparison of Methods (‘Four Cell’ Matrix)
Low Turbulence
High Turbulence
High Wind Speed
Low Wind Speed
Baseline
REWS
Turb Corr
REWS & Turb Corr
Power Dev Matrix
Baseline
REWS
Turb Corr
REWS & Turb Corr
Power Dev Matrix
Better
Better
Worse
Seek to determine which methods work well when.
PCWG-Share-2 to expand upon these results.
Worse
Percentage Reduction in Error

## Slide 12
PCWG-Share-1
≈50 participant datasets (4 remote sensing datasets)
3 method tested (REWS, IEC Turbulence Correction & Power Deviation Matrix)
Calculation Issues: Interpolation Errors and Erroneous Outliers
PCWG-Share-X Timeline
Dec 2015
Sept2016
Oct to
Dec
2016
PCWG-Share-1.1
≈44 participant datasets (11 remote sensing datasets)
Same 3 method tested (REWS, IEC Turbulence Correction & Power Deviation Matrix)
Streamlined participation process
PCWG-Share-1 Calculation Issues Resolved
PCWG-Share-2
Target: 100 participant datasets (25 remote sensing datasets)
Additional methods to be tested e.g. 3D Power Deviation Matrix & REWS with Upflow
Refined results analysis
Behind Schedule, sorry! (more later)

## Slide 13
IEC 61400-12-1 Ed 2
Getting Ready for the New Standard
PCWG: Uncertainty Worked Examples
IEA Task 32: Uncertainty Round Robin

## Slide 14
IEC 61400-12-1 Edition 2 Status
The PCWG in collaboration with IEA Task 32 are seeking to build industry understanding of the new Power Performance Standard. www.pcwg.org.
Document Stage | Document Stage Description | IEC61400-12-1 Ed 2 Status
CDV Committee Draft for Voting | Feedback Stage: Document is sent to the various National Committees for comment. Once the feedback is received the TC (Technical Committee) integrated the feedback and prepares the FDIS. | Completed
FDIS Final Draft International Standard | Approval Stage: Document is sent to the National Committees for voting. At this stage no comments or requests for change are accepted although typographical errors can be pointed out for correction by IEC prior to publication. If, after the FDIS vote, the publication is approved, no more changes of a technical nature can be made to it. Only obvious editorial mistakes can be corrected. | Complete (Nov 2016)
Publication of IS (International Standard) | Final Stage: The IEC generates the cover pages and prepares the document for publication. The document is published and put on sale in the IEC Web Store. Note that editorial errors not captured prior to publication can still be issued as corrigendum by IEC throughout the life of a specific publication. | Expected Early 2017

## Slide 15
IEA Task32 & PCWG Activities Timeline (2016)
Distribution of round robin dataset and instructions to participants.
Initial round robin results presented at Pamplona and Minneapolis PCWG meetings.
Second round robin initiated, results due by end of October.
Collation of final results
Presentation of final results at PCWG meeting in Glasgow.
IEC Round Robin
IEC Worked Examples
Preparation of work examples.
Presentation of full suite of worked examples at September PCWG Meetings. Release of worked examples on PCWG DropBox.
IEA32 & PCWG members to review worked examples and provide feedback.
Public publication of work examples after Dec PCWG meeting (www.pcwg.org)
Jul & Aug
Sept
Oct
Nov
Dec

## Slide 16
Agenda Overview
13 December 2016

## Slide 17
09.30 - 10.00 Introductions & Welcome
  09.30 - 09.40 Welcome from our hosts, Owen Murphy, ORE Catapult
  09.40 - 10.00, PCWG Update/Overview, Peter Stuart (RES)
10.00 - 11.00: PCWG-Share-X Results (Intelligence Sharing Initiative),
  10.00 - 10.40: Results Presentation, Peter Stuart (RES) & Andy Clifton (NREL)
  10.40 - 11.00: Q&A
11.00 - 11.10: Coffee Break
11.10 - 11.25: Machine Learning Sub Group Presentation, Andy Clifton (NREL)
Agenda Overview (Morning)

## Slide 18
11.25 - 12.20: Preparing for 61400-12-1 Ed 2
  11.25 – 11.40: 12-1 Ed 2 Round Robin Results Overview, Luke J Simmons, DNV GL
  11.40 – 11.55: 12-1 Ed 2 Work Examples Overview, Lee Cameron, RES
  11.55 – 12.10: 12-1 Ed 2 Worked Examples Feedback, Axel Albers, WindGuard
  12.10 – 12.20: Q&A
12.20 – 13.00: Morning Presentation Session:
  12.20 – 12.35: “Nacelle Lidar measurements of the Induction Zone from Multiple Offshore Wind Farms”, Frederik Brink, Dong Energy
  12.35 – 12.40: Q&A
  12.40 – 12.55: “Turbine performance – Veer”, Matthew Colls, Prevailing
  12.55 – 13.00: Q&A
Agenda Overview (Morning & Early Afternoon)

## Slide 19
13.00 - 14.00: Lunch
14.00 - 14:40: Afternoon Presentation Session:
  • 14.00 – 14.15: “Evaluating The Wind Resource From Rotor Equivalent Wind Speeds.”, Christiane Montavon , ANSYS
  • 14.15 – 14.20: Q&A
  • 14.20 – 14.35: ‘Blade Leading Edge Erosion Project‘, Owen Murphy, ORE Catapult
  • 14.35 – 14.40: Q&A
Agenda Overview (Afternoon)
14.40 - 15.00: Break & Adaptive Problem Exercise
15.00 - 16:00 Afternoon Discussion Session:
  • The Future of the PCWG
  • PCWG-Share-X Next Steps
16.00 – 16.30: Wrap Up

## Slide 20
Join the Power Curve Working Group at: www.pcwg.org

## Slide 21
Priority Actions (what we are working on right now)
Note: as IEA Task 32 also planned a IEC61400-12 Round Robin the PCWG has focused on worked examples.