## Slide 1
PCWG 2017 Roadmap
Friday, 09 June 2017
Copenhagen, Denmark
Peter Stuart

## Slide 2
We’ve Always Known that Real World Wind Turbine Performance is NOT as Simple as Power=P(v, ρ)!
Extract from C.J. Christensen et al: ”Accuracy of power curve measurements”, Risø-M-2632, 1986...
”… The power curve is then seen as the relation between the power P(v) produced by this undisturbed wind v.
This definition is, however, of very doubtful value for a windmill in the natural wind. The main difficulty is that it assumes a smooth laminar flow of high degree of homogeneity and symmetry”
Power (P)
Wind Speed (v)
P=P(v, ρ)
ρ = Air Density
The PCWG aims to build industry consensus on how best to predict real world turbine performance and look beyond P=P(v, ρ). www.pcwg.org.

## Slide 3
Categories of Turbine Performance Corrections
Inner Range Performance
Adjustments to reflect the fact that even under warranted/ideal conditions performance may not be 100%
Outer Range Performance
Adjustments to reflect the fact that turbine performance may deviate from Inner Range behaviour in Outer Range Conditions
e.g. Low/High TI, Low/High Shear etc.
Note: The PCWG Inner-Outer Range Proposal is Conceptual Decomposition, and does infer specific parameter ranges.
Reflecting the Real World: Inner-Outer Range Decomposition
+ Other Performance Corrections
Icing, Blade Degradation, Sub-optimal performance etc.
Inner Range
Outer Range
PCWG Activities

## Slide 4
Categories of Turbine Performance Corrections
Average Performance
(Bulk) Adjustments to reflect the fact that on average (in all conditions) turbines may not meet their documented performance level
Conditions Specific Performance
Adjustments to reflect the fact that turbine performance may deviate from average performance in ‘non-average’ Conditions
e.g. Low/High TI, Low/High Shear etc.
Reflecting the Real World: Average-Specific Decomposition
+ Other Performance Corrections
Icing, Blade Degradation, Sub-optimal performance etc.
PCWG Activities
Remove Bias
Remove Uncertainty
Improve Project Design

## Slide 5
Inner Range Performance
Average Performance
Classification of PCWG Activities by Component
Outer Range Performance
Conditions Specific Performance
Note: whilst the two decompositions are subtly different, they are broadly compatible with respect to the roadmap e.g. actions to further ‘Inner Range’ understanding, will generally further ‘Average Performance’ understanding.
The type of PCWG activates differs strongly depending on the problem component
The PCWG is seeking to define an assessment framework to define how to make best use of historic power performance tests when predicting future inner/average performance.
The PCWG is attempting to evaluate quantitative methods for predicting Outer/ Specific performance via the PCWG Intelligence Sharing Initiative (PCWG-Share-X)

## Slide 6
Reflecting the Real World: Inner Range / Average Performance
Extract from ‘High Resolution Turbine-Specific Matrix’, Carl Ostridge DNV GL,
Colorado PCWG Meeting, 10 August 2016, download from www.pcwg.org.

## Slide 7
Turbulence Intensity [%]
Wind Speed [m/s]
Colour = % Observed Power Deviation
(Observed - Base)
Power (P)
Wind Speed (v)
P=P(v, ρ)
Inner Range Performance
Outer Range Deviations (Observed – Base)
High TI & High V
Negative Deviation
Low TI & Low V
Negative Deviation
High TI & Low V
Positive Deviation
Reflecting the Real World: Outer Range Performance

## Slide 8
PCWG 2017 Roadmap

## Slide 9
PCWG 2017 Roadmap
Roadmap Page 1/4
Define best practice guidelines for stakeholder data exchange and analysis to establish inner/average performance
Objectively determine/refine the best methods for modelling outer/specific performance using the PCWG-Share-X Platform
1. Inner/Average Performance
2. Outer/Specific Performance
OUTCOME
50% reduction in outer/specific modelling uncertainty
→ Reduced Investor Risk
Evidence Pathway for Inner/Average Performance
→ Reduced Investor Risk
NOW
End of 2017
Publically available worked Examples
PCWG Analysis Tool Development
3. Enabling Activities
The right tools & industry understanding to deliver items 1 & 2

## Slide 10
PCWG 2017 Roadmap
Roadmap Page 4/4
Define best practice guidelines for stakeholder data exchange and analysis to establish inner/average performance
1. Inner/Average Performance
2017 - Timeline
Draft Guidelines Document (based on a overhaul of existing DRAFT ‘guidelines for preparation of a turbine information pack’ document).
Aug
Dec
Feedback
Sep
Oct
Updated Draft Document
Final Feedback
Nov
Publication on PCWG Website

## Slide 11
Roadmap Page 3/4
2017 - Timeline
PCWG-Share-2
PCWG-Share-3
PCWG-Share-4
June
Aug
Oct
2. Outer/Specific Performance

## Slide 12
PCWG 2017 Roadmap
Roadmap Page 4/4
Publically Available Worked Examples
  IEC Worked Examples
  Non-IEC Worked Examples e.g. Production by Height, Marmander Interpolation etc.
PCWG Analysis Tool Development
  Implementation of New Methods
  Improved Testing and worked examples
  Improved Beta Testing (Beta Testing Sub Group)
  Improved Documentation (Beta Testing Sub Group)
Machine Learning
  Sub-group meetings and discussions
  Creation of Machine Learning Web Service for PCWG-Share-4
Publish Summary of PCWG Activities & Outcomes (on PCWG Website)
3. Enabling Activities

## Slide 13
Questions/Discussion