## Slide 1: Proposal of a new power data format - motivation & draft -
Presenter:
Lasse Svenningsen

## Slide 2
Outline
Current PC format…
…Challenges
…A solution
Draft of a new power data format
Use of new format?
Summary, limitations & alternative
Next steps: feedback & input needed

## Slide 3
Typical AEP calculations
Current PC format

## Slide 4
Typical AEP calculations
Available data:
Power and Ct curve at std. conditions* for a set of air densities
Power (and Ct?) at std. air density and conditions and for a set of noise modes
1/3 octave band data of source noise for each of the noise modes
*) May be site specific (TI, shear, ..)
Current PC format

## Slide 5
Typical AEP calculations
Available data:
Power and Ct curve at std. conditions* for a set of air densities
Power (and Ct?) at std. air density and conditions and for a set of noise modes
1/3 octave band data of source noise for each of the noise modes
Format:
Typically, tables in a pdf or excel
*) May be site specific (TI, shear, ..)
Current PC format

## Slide 6
Typical AEP calculations
Available data:
Power and Ct curve at std. conditions* for a set of air densities
Power (and Ct?) at std. air density and conditions and for a set of noise modes
1/3 octave band data of source noise for each of the noise modes
Format:
Typically, tables in a pdf or excel
Possible corrections:
E.g. IEC61400-12-1 ed. 2 corrections for rho, TI, shear, etc.
*) May be site specific (TI, shear, ..)
Current PC format

## Slide 7
Current challenges:
Many turbines run wholly or partly in “Special Operation Modes” (SOM)
- E.g.: Noise, Load, Power/Boost, High/low temp., (High wind), …
Challenges

## Slide 8
Current challenges:
Many turbines run wholly or partly in “Special Operation Modes” (SOM)
- E.g.: Noise, Load, Power/Boost, High/low temp., (High wind), …
SOM’s are not ‘power optimal’ (→ standard corrections do not work)
Challenges

## Slide 9
Current challenges:
Many turbines run wholly or partly in “Special Operation Modes” (SOM)
- E.g.: Noise, Load, Power/Boost, High/low temp., (High wind), …
SOM’s are not ‘power optimal’ (→ standard corrections do not work)
III) The effect/benefit of the SOM on AEP is not quantified
- Manufacturers or consultants need to show the added value or limited loss
Challenges

## Slide 10
Current challenges:
Many turbines run wholly or partly in “Special Operation Modes” (SOM)
- E.g.: Noise, Load, Power/Boost, High/low temp., (High wind), …
SOM’s are not ‘power optimal’ (→ standard corrections do not work)
III) The effect/benefit of the SOM on AEP is not quantified
- Manufacturers or consultants need to show the added value or limited loss
IV) Manual copy paste from e.g. pdf’s, increase risk of human errors
Challenges

## Slide 11
Main ideas for a solution:
Power data MUST include full dependence on relevant climate variables
A Solution

## Slide 12
Main ideas for a solution:
Power data MUST include full dependence on relevant climate variables
Power data MUST include ‘reference mode’ to quantify effect of SOM’s
A Solution

## Slide 13
Main ideas for a solution:
Power data MUST include full dependence on relevant climate variables
Power data MUST include ‘reference mode’ to quantify effect of SOM’s
All the relevant data/info compiled in one file
A Solution

## Slide 14
Basic assumptions/decisions:
Self-contained and ~self-explained format
A Solution

## Slide 15
Basic assumptions/decisions:
Self-contained and ~self-explained format
Keep math as simple as possible, to ensure 100% reproducibility
A Solution

## Slide 16
Basic assumptions/decisions:
Self-contained and ~self-explained format
Keep math as simple as possible, to ensure 100% reproducibility
Special operation modes mutually exclude each other (or fixed combination)
A Solution

## Slide 17
Basic assumptions/decisions:
Self-contained and ~self-explained format
Keep math as simple as possible, to ensure 100% reproducibility
Special operation modes mutually exclude each other (or fixed combination)
Wind shear can be handled as explicit parameter or using REWS
A Solution

## Slide 18
The basic outline:
A single zip-file containing:
Draft of a new format

## Slide 19
The basic outline:
A single zip-file containing:
  XML-file with basic info, list of SOMs and climate variables
  II) Mat files for each SOM giving power or Ct dependence of climate variables
Draft of a new format

## Slide 20
The basic outline:
A single zip-file containing:
  Keeps everything together, yet easy to extract/view
  Encryption + license protection in windPRO optional for project specific use
  XML-file with basic info, list of SOMs and climate variables
  II) Mat files for each SOM giving dependence of climate variables
Draft of a new format

## Slide 21
The basic outline:
A single zip-file containing:
  XML-file with basic info, list of M SOMs and N climate variables
  - Structured
  - Human readable
  - Extendable
  II) Mat files for each SOM giving dependence of N climate variables
Draft of a new format

## Slide 22
The basic outline:
A single zip-file containing:
  XML-file with basic info, list of SOMs and climate variables
  II) 2 Mat files for each of M SOM’s giving dependence of N climate var.
    - 1 Mat file = 1 data matrix (with N dimensions)
    - Standard binary data format, supported by Matlab, Python, R, …
    - Power versus N relevant climate variables
    - Ct versus N relevant climate variables
    (- Source noise versus 1/3-octave band and wind speed)
Draft of a new format

## Slide 23
The XML file:
Draft structure (xml schema)
Draft of a new format

## Slide 24
The XML file:
Draft structure (xml schema)
Draft of a new format

## Slide 25
The XML file:
Draft structure (xml schema)
Draft of a new format

## Slide 26
The XML file:
Draft structure (xml schema)
Draft of a new format

## Slide 27
The XML file:
Draft structure (xml schema)
Draft of a new format

## Slide 28
The Mat files:
One mat file for power and one for Ct, for each SOM
Draft of a new format

## Slide 29
The Mat files:
One mat file for power and one for Ct, for each SOM
Each mat file has N dimensions, representing N climate variables
Draft of a new format

## Slide 30
The Mat files:
One mat file for power and one for Ct, for each SOM
Each mat file has N dimensions, representing N climate variables
Draft of a new format
  Example N=3 climate dimensions, power matrix:

## Slide 31
The Mat files:
One mat file for power and one for Ct, for each SOM
Each mat file has N dimensions, representing N climate variables
Draft of a new format
Wind speed (i)
Air density (j)
Turbulence (k)
Power values (pi,j,k)
Pi,j,k
P1,1,1
  Example N=3 climate dimensions, power matrix:

## Slide 32
How to ‘extract’ power or Ct values
ONLY via multi-linear interpolation in defined parameter order
Use of power and Ct matrices

## Slide 33
How to ‘extract’ power or Ct values
ONLY via multi-linear interpolation in defined parameter order
Extrapolation NOT allowed, truncation at the ‘edges’
Use of power and Ct matrices

## Slide 34
Simple example 1:
Modes: {‘Mode 0 (reference)’, ‘Noise 1’, ‘Noise 2’, ‘Noise 3’}
Climate variables: {Wind speed, Air density, Turbulence}
Parameters: {Power, Ct}
I.e.:
  4 power Mat-files each with 3 climate dimensions
  4 Ct Mat-files each with 3 climate dimensions
Use of power and Ct matrices

## Slide 35
Simple example 1 cont’d:
Operation strategy, turbine X:
Mode 0: 08-16h
Noise 1: 16-20h
Noise 3: 20-08h
AEP calculation:
in each time step find mode from turbine strategy (set at each WTG)
extract power and Ct for mode using wind speed, air density, turbulence
extract power and Ct for ref. mode using wind speed, air density, turbulence
etc. …
Use of power and Ct matrices

## Slide 36
Simple example 2:
Modes: {‘Reference’, ‘Boost’, ‘Load’}
Climate variables: {Wind speed, Air density, Turbulence, Shear}
Parameters: {Power, Ct}
I.e.:
  3 power Mat-files each with 4 climate dimensions
  3 Ct Mat-files each with 4 climate dimensions
Use of power and Ct matrices

## Slide 37
Simple example 2 cont’d:
Operation strategy, turbine Y:
Reference: If not below
Boost: TI≤0.16 & u≥12m/s & dir ∈{15; 170}
Load: TI≥0.22
AEP calculation:
in each time step find mode from turbine strategy (set at each WTG)
extract power and Ct for mode using wind speed, air density, turbulence
extract power and Ct for ref. mode using wind speed, air density, turbulence
etc. …
Use of power and Ct matrices

## Slide 38
How do you make the Mat files?:
Up to the individual manufacturers!
Could be based on aero-elastic simulations
Could be based on in-house PC correction models
Could even be based on measurements or basically anything!
Use of power and Ct matrices

## Slide 39
Summary:
Many turbines run partly/wholly in ‘SOM’
Standard corrections don’t necessarily apply
A reference mode important to quantify effect of ‘SOM’
Our proposed format: simple math, ensure reproducibility
=> a more complete set of self-explained data
Summary, limitations & alternative

## Slide 40
Summary:
Many turbines run partly/wholly in ‘SOM’
Standard corrections don’t necessarily apply
A reference mode important to quantify effect of ‘SOM’
Our proposed format: simple math, ensure reproducibility
=> a more complete set of self-explained data
Limitations:
Cannot directly handle hysteresis behaviour
Controller behaviour must be reflected in the power/Ct data
Wind profile parameterised via shear exponent (could be handled)
Summary, limitations & alternative

## Slide 41
Summary:
Many turbines run partly/wholly in ‘SOM’
Standard corrections don’t necessarily apply
A reference mode important to quantify effect of ‘SOM’
Our proposed format: simple math, ensure reproducibility
=> a more complete set of self-explained data
Limitations:
Cannot directly handle hysteresis behaviour
Controller behaviour must be reflected in the power/Ct data
Wind profile parameterised via shear exponent (could be handled)
Alternative?:
An interface to ‘black box’ dlls…
Summary, limitations & alternative

## Slide 42
We need feedback:
Questions/suggestions are much welcome!
At a short web meeting in the no too distant future?
- Interested? Please mail: LS@emd.dk or give me a business card.
With today’s input we will make a draft documentation + example
- We can send that out prior to a web-meeting.
Can be available in windPRO 3.2 in a first version.
Next steps

## Slide 43
Thanks for your attention!
The End