## Slide 1: Power Curve Working Group What are the issues?
Daniel Stevens
Resource Assessment, SSE Renewables
04 December 2012

## Slide 2: The issues
  Power performance in the real world
  Mitigating the risk of underperformance
  Working closer
  SSE Renewables welcomes the formation of this Working Group!

## Slide 3: 1) Power performance in the real world

## Slide 4: Weak performance: identifying, predicting
Wind Farm level
WTG
level
Establishing cause
Quantifying AEP impact
Performance tracking using 10 minute data: the ‘APA’ team in SSE

## Slide 5: Establishing reasons for underpeformance
Quantifying impact of conditions on power performance
CFD and Remote Sensing both have a role to play
Expensive
e.g. Fairburn inflow angle study
Validation across many sites required to inform loss factors

## Slide 6: Turbine suitability analysis
  Excessive turbine fatigue loads are caused by:
    High/negative shear
    High turbulence (ambient, wake induced)
    High inflow angle
  Mitigated by moving WTGs or curtailing/load control systems
  Just because a WTG location is warranted, doesn’t mean it is optimal!
  SSE have evidence of OEMs curtailing/‘turning down’ a turbine’s power curve despite location getting a “clean MLA”
  These adjusted power curves eventually become the norm
   Feed into production based AEPs
   Reduced NPV/IRR
   Increases refinancing/divestment risk

## Slide 7: Can we blame OEMs?
  No OEM wants to have to turn down WTGs (reputation, yield)
  Done to avoid excessive vibration trips hitting availability targets – which client uses as an incentive to the OEM
  And to avoid this happening:
  A clean MLA and high AEP wins tenders
  MLA only as good as the data, the model and the scenario
  We need more open and honest communication

## Slide 8: 2) Mitigating the risk of underperformance

## Slide 9: Warranties and IPCTs
  Traditional approach to mitigating risk
  SSE current policy is to test each new turbine model bought
  Decision to test according to IEC 61400-12-1 (via an IPCT) is made according to risk profile of site (size, technology)
6 IPCTs carried out by SSE to date
All in moderate – complex terrain
“Successfully” argued against testing > 1 WTG
Average efficiency: ~98%, this appears to match the industry average*
  Is this still a sufficient way of mitigating risk?
  * EWEA Lyon, July 2012, Keir Harman (GLGH)

## Slide 10: Independent Power Curve Tests
Achieving IEC-61400-12-1 compliance rarely straightforward
Site calibrations the norm for SSE sites
Sectors restricted by shear, inflow, turbulence characteristics
E.g. Clyde
* EWEA Lyon, July 2012, Keir Harman (GLGH)

## Slide 11: Independent Power Curve Tests (2)
An IPCT doesn’t mitigate the risk of underperformance
    Only based on 1 or a few WTGs
    IPCT always achieves > 95%; (100% - uncertainty)
    OEM can (and does) change pitch/rpm settings during WOM
OEM often demands multiple test WTGs to mitigate risk  £££
Benefits: provides testers with a body of evidence for making pragmatic adjustments to AEPs
How to test Intelligent power control systems? Settings can change every 10 minutes!

## Slide 12: Alternative means of mitigating risk
  Move to yield-based warranties?
    Involves a shift in paradigm away from incentivising high availability
  Operator’s Power Curve Tests
    A more flexible approach to ‘IEC conditions’  more representative of actual conditions
    Use of Remote sensing
    Accept it won’t form the basis of a warranty
  Apply pragmatic adjustments to AEPs
    As an uncertainty or a loss factor?
  Through better site design
  We need more open and honest communication between Developers and OEMs

## Slide 13
3) Working closer

## Slide 14: Working closer
  Ideal: involve OEM in early design work  commercially feasible?
  Ambition: Move away from MLA being a black box...
  RISK SHARING APPROACH
  Developer provides LT wind climate at each WTG
    CFD, RS, Lidar overfly data: not just raw mast data
    Careful consideration given to which scenario presented
  OEM works with developer to deliver:
    realistic power curves for WF lifetime
    optimised control strategy for yield, loading, noise.
    Best and worst case scenarios presented (if applicable)
  Resulting AEP is a hybrid of both parties’ expertise
    Consultant provides DD
Notes:   Avoid discrepancies between OEM & Developer’s AEP
  Further incentives needed?

## Slide 15: Intelligent Power Control Systems
2 key types:
Load control systems 2. Yield improvement systems (OWFs)
Former monitors and manages lifetime load cycle consumption. Allows WTG design envelope to be pushed.
Both controlled by sensors in turbine detecting onerous/advantageous wind conditions and selecting power curves on sub 10 minute basis.
Excluded from IPCTs
Little guidance on how to predict impact on AEP
Difficult to assess actual impact
Certification challenging

## Slide 16: Conclusions
  Not all sites look like Høvsøre!
  Warranties only offer limited assurance
  Quantifying effects of onerous wind conditions on
  power performance is challenging
  Incentivising availability can sacrifice yield
  MLAs have been too ‘black box’ to date
  Turbines are getting cleverer
  All parties have the ability to effect improvements