## Slide 1: 3D Power Deviation Matrix
PCWG Meeting – New Orleans, LA. September 14, 2015
Alex Head

## Slide 2
Define turbine performance outside of Inner Range using a single parameterized model:
  A single model applicable globally
  Spanning variations in geometry of turbines
  Across all site conditions
Target Parameters
Parameters must capture physical drivers
To be used to predict turbine performance with pre-construction mast data.

## Slide 3: Resulting parameter set
Compensate for variations in turbine geometry, controller effects and link to aerodynamic theory – Lift to Drag Ratio
Turbulence
  A factor in blade Lift to Drag performance
Rotor wind speed ratio
  Correlates with angle of attack variation across rotor
  Captures impact of diameter, hub height and shear
Normalised wind speed
  Wind speed affects blade Lift to Drag performance
  Normalised by the zero TI rated speed to align controller modes across turbine types.

## Slide 4: Data set
Normalised wind speed
RWSR
Turbulence
Resulting 3D performance matrix
 | 2% | 4% | 6% | 8% | 10% | 12% | 14% | 16% | 18% | 20% | 22% | 24%
1.7 | 72% | 73% | 75% | 79% | 79% | 80% | 82% | 71% |  |  |  | 
1.6 | 71% | 75% | 78% | 79% | 81% | 83% | 82% | 85% | 78% |  |  | 
1.5 | 72% | 76% | 78% | 82% | 85% | 85% | 84% | 85% | 86% | 83% | 95% | 
1.4 | 72% | 75% | 81% | 85% | 85% | 84% | 84% | 89% | 90% | 92% | 94% | 95%
1.3 | 75% | 76% | 80% | 84% | 86% | 85% | 90% | 92% | 92% | 98% | 98% | 108%
1.2 | 73% | 77% | 84% | 87% | 89% | 92% | 95% | 100% | 105% | 105% | 108% | 114%
1.1 | 73% | 78% | 86% | 90% | 95% | 99% | 106% | 109% | 110% | 112% | 114% | 117%
1.0 | 73% | 80% | 87% | 91% | 101% | 101% | 105% | 108% | 110% | 117% | 118% | 124%
0.9 |  | 72% | 85% | 89% |  | 91% | 92% | 91% | 97% | 101% | 100% | 107%
0.8 |  |  |  |  |  |  | 88% | 87% | 82% | 89% | 91% | 97%
0.7 |  |  |  |  |  |  | 85% | 84% | 82% | 84% | 87% | 
Unorm= 0.5
Unorm= 0.9
 | 2% | 4% | 6% | 8% | 10% | 12% | 14% | 16% | 18% | 20% | 22% | 24%
1.7 | 85% | 88% | 87% | 92% |  |  |  |  |  |  |  | 
1.6 | 84% | 92% | 99% | 92% | 97% |  |  |  |  |  |  | 
1.5 | 85% | 93% | 96% | 95% | 94% | 102% | 98% |  |  |  |  | 
1.4 | 86% | 94% | 96% | 97% | 99% | 100% | 100% | 101% | 105% | 105% |  | 
1.3 | 87% | 94% | 95% | 98% | 99% | 101% | 101% | 102% | 102% | 102% | 102% | 
1.2 |  | 95% | 96% | 98% | 99% | 101% | 102% | 102% | 102% | 103% | 102% | 101%
1.1 | 98% | 95% | 93% | 98% | 100% | 100% | 102% | 102% | 102% | 103% | 103% | 
1.0 |  |  |  | 97% | 101% | 101% | 102% | 102% | 103% | 105% |  | 
0.9 |  |  |  |  | 96% | 100% | 100% | 97% | 92% | 93% |  | 
0.8 |  |  |  |  | 94% | 96% | 94% | 96% | 89% |  |  | 
0.7 |  |  |  |  |  |  | 94% | 90% | 86% |  |  | 
Turbulence
Turbulence
RWSR
RWSR
Inner Range
Inner Range