## Slide 1: How to Improve Energy Predictions?
4th December 2012 Andrew Tindal, SVP Head of Energy

## Slide 2
Why do we need to improve?
For wind to compete in the global energy market we need trust
Trust from Developers / Owners to take projects forward
Trust from Financiers to put money into wind projects
Wind already has the challenge of wind variability to deal with
This has the potential to give Owners / Financiers surprises
Need to reduce other potential sources of surprises
Power curves are a potential source of surprises
There are complex technical issues to deal with
Unlike wind variability the issues are under the control of our industry

## Slide 3
What about warranties?
Focus of this presentation is how we can improve predictions
It would be naive to ignore the fact that power curves are subject to warranty arrangements – but these are commercial arrangements – and are outside the direct scope of this presentation
To make progress need to consider how predictions can be improved by better modelling the science of what is going on

## Slide 4: The current power curve model
Input
Wind speed
Air density
Site wind conditions
Energy prediction
Power curve
Current power curve variables:
Output

## Slide 5: In reality the situation is more complex – core issues
Input
Output
Wind speed
Air density
Site wind conditions
Energy prediction
Power curve
Additional power curve variables
Turbulence
Wind shear
Inflow angle
Anemometer characteristics
These parameters vary with effects of terrain, roughness, atmospheric conditions and wakes of other turbines
Site measurements may use different sensors from sensors assumed for sales power curve

## Slide 6: There are other issues which impact power performance
Input
Output
Site wind conditions
Energy prediction
Power curve
Power curve – additional issues which impact energy prediction
Hysteresis algorithms
  Cut in parameters
  Cut out parameters
Sub-optimal performance
  Sensor issues
  Software issues
  Other issues
Curtailment
  Loads
  Power
  Environmental
Blade issues
  Fouling
  Icing
  Surface degradation

## Slide 7: What would help improve predictions?
Theme 1 – Definition of the problem
Agreement of the variables to which a power curve is sensitive

## Slide 8: What would help improve predictions?
Theme 2 – A clear starting point
A specific definition of the conditions for which a sales power is representative
Improved knowledge of the information used to define the sales power curve

## Slide 9: What would help improve predictions?
Theme 3 – Improved models and measurements
Improved models to allow power curves to be adjusted on a site specific basis for all variables to which a power curve is sensitive
Changing site specific measurement campaigns to provide better data as inputs to power curve adjustment models

## Slide 10: What would help improve predictions?
Theme 4 – Information to improve models for “additional issues”
Improved information exchange to better model:
              Curtailment
              Hysteresis algorithms
              Blade issues
              Sub-optimal performance

## Slide 11: Questions? Discussion to be continued in afternoon